## Slide 1: Chapter 3 Transport Layer
Slides are adapted from those of by J.F Kurose and K.W. Ross with copyright 1996-2020 J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: Chapter 3 Transport Layer
our goals:
understand principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
learn about Internet transport layer protocols:
  UDP: connectionless transport
  TCP: connection-oriented reliable transport
  TCP congestion control

## Slide 3
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
3.6 principles of congestion control
3.7 TCP congestion control
Chapter 3 Transport Layer
Transport Layer

## Slide 4
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
3.6 principles of congestion control
3.7 TCP congestion control
Chapter 3 Transport Layer
Transport Layer

## Slide 5: Transport services and protocols
provide logical communication between app processes running on different hosts
transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
more than one transport protocol available to apps
  Internet: TCP and UDP
3.1 transport-layer services
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport
Notes: segment: 报文段

## Slide 6: Transport vs. network layer
network layer: logical communication between hosts
transport layer: logical communication between processes
  relies on, enhances, network layer services
12 kids in Ann's house sending letters to 12 kids in Bill's house:
hosts = houses
processes = kids
app messages = letters in envelopes
transport protocol = Ann and Bill who demux to in-house siblings
network-layer protocol = postal service
household analogy:
3.1 transport-layer services

## Slide 7: Internet transport-layer protocols
reliable, in-order delivery (TCP)
  congestion control
  flow control
  connection setup
unreliable, unordered delivery: UDP
  no-frills extension of "best-effort" IP
services not available:
  delay guarantees
  bandwidth guarantees
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport
3.1 transport-layer services

## Slide 8
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
3.6 principles of congestion control
3.7 TCP congestion control
Chapter 3 Transport Layer
Transport Layer

## Slide 9: Multiplexing/demultiplexing
process
socket
use header info to deliver
received segments to correct
socket
demultiplexing at receiver:
handle data from multiple
sockets, add transport header (later used for demultiplexing)
multiplexing at sender:
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3
3.2 multiplexing and demultiplexing

## Slide 10: How demultiplexing works
host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries one transport-layer segment
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(payload)
other header fields
TCP/UDP segment format
3.2 multiplexing and demultiplexing

## Slide 11: Connectionless demultiplexing
recall: created socket has host-local port #:
when host receives UDP segment:
  checks destination port # in segment
  directs UDP segment to socket with that port #
recall: when creating datagram to send into UDP socket, must specify
  destination IP address
  destination port #
IP datagrams with same dest. port #, but different source IP addresses and/or source port numbers will be directed to same socket at dest
3.2 multiplexing and demultiplexing
DatagramSocket mySocket1 =
newDatagramSocket（12534）；

## Slide 12: Connectionless demux: example
DatagramSocket serverSocket
= new DatagramSocket (6428);
transport
application
physical
link
network
P3
transport
application
physical
link
network
P1
transport
application
physical
link
network
P4
DatagramSocket mySocket1 = new DatagramSocket (5775);
DatagramSocket mySocket2 = new DatagramSocket (9157);
source port: 9157
dest port: 6428
source port: 6428
dest port: 9157
source port: ?
dest port: ?
source port: ?
dest port: ?
3.2 multiplexing and demultiplexing

## Slide 13: Connection-oriented demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
demux: receiver uses all four values to direct segment to appropriate socket
server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
web servers have different sockets for each connecting client
  non-persistent HTTP will have different socket for each request
3.2 multiplexing and demultiplexing

## Slide 14: Connection-oriented demux: example
transport
application
physical
link
network
P3
transport
application
physical
link
P4
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
network
P6
P5
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
three segments, all destined to IP address: B,
dest port: 80 are demultiplexed to different sockets
server: IP address B
3.2 multiplexing and demultiplexing

## Slide 15: Connection-oriented demux: example
transport
application
physical
link
network
P3
transport
application
physical
link
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
server: IP address B
network
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
P4
threaded server
3.2 multiplexing and demultiplexing

## Slide 16
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
3.6 principles of congestion control
3.7 TCP congestion control
Chapter 3 Transport Layer
Transport Layer

## Slide 17: UDP: User Datagram Protocol [RFC 768]
"no frills," "bare bones" Internet transport protocol
"best effort" service, UDP segments may be:
  lost
  delivered out-of-order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
UDP use:
  streaming multimedia apps (loss tolerant, rate sensitive)
  DNS
  SNMP
reliable transfer over UDP:
  add reliability at application layer
  application-specific error recovery!
  approach taken in HTTP/3
  google QUIC over HTTP/3
3.3 connectionless transport: UDP
https://datatracker.ietf.org/doc/draft-ietf-quic-http/?include_text=1
Notes: SNMP：simple network management protocol, application layer

## Slide 18: UDP: segment header
source port #
dest port #
32 bits
application
data
(payload)
UDP segment format
length
checksum
length, in bytes of UDP segment, including header
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small header size
no congestion control: UDP can blast away as fast as desired
why is there a UDP?
3.3 connectionless transport: UDP

## Slide 19: UDP checksum
sender:
treat segment contents, including header fields, as sequence of 16-bit integers
checksum: addition (one's complement sum) of segment contents
sender puts checksum value into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later ….
Goal: detect "errors" (e.g., flipped bits) in transmitted segment
3.3 connectionless transport: UDP

## Slide 20: Internet checksum: example
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
3.3 connectionless transport: UDP
https://www.cnblogs.com/noble/p/4144139.html
example: add two 16-bit integers
sum
checksum
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
Notes: Kurose and Ross forgot to say anything about wrapping the carry and adding it to low order bit
wrapped around
carryout: 进位

## Slide 21
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
3.6 principles of congestion control
3.7 TCP congestion control
Chapter 3 Transport Layer
Transport Layer

## Slide 22: Principles of reliable data transfer
important in application, transport, link layers
  top-10 list of important networking topics!
3.4 principles of reliable data transfer
sending
process
data
data
reliable channel
receiver
process
transport
layer
application
layer
Notes: characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 23: Principles of reliable data transfer
important in application, transport, link layers
  top-10 list of important networking topics!
3.4 principles of reliable data transfer
sending
process
data
data
reliable channel
receiver
process
transport
layer
application
layer
Notes: characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 24: Principles of reliable data transfer
important in application, transport, link layers
  top-10 list of important networking topics!
3.4 principles of reliable data transfer
sending
process
data
data
reliable channel
receiver
process
transport
layer
application
layer
Notes: characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 25: Principles of reliable data transfer
3.4 principles of reliable data transfer
sending
process
data
data
reliable channel
receiver
process
transport
layer
application
layer
unreliable channel
(a) reliable service abstraction
(b) reliable service implementation
network
layer
important in application, transport, link layers
  top-10 list of important networking topics!
Notes: characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 26: Principles of reliable data transfer
(a) reliable service abstraction
3.4 principles of reliable data transfer
sending
process
data
data
reliable channel
receiver
process
transport
layer
application
layer
unreliable channel
data
data
reliable data
transfer protocol
(sender side)
reliable data
transfer protocol
(receiver side)
rdt_send ( )
deliver_data ( )
udt_send ( )
rdt_rcv ( )
network
layer
important in application, transport, link layers
  top-10 list of important networking topics!
Complexity of reliable data transfer protocol will depend (strongly) on characteristics of unreliable channel (lose, corrupt, reorder data?)
sending
process
data
data
receiver
process
(b) reliable service implementation
Notes: characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 27: Reliable data transfer protocol (rdt): getting started
sender
side
receiver
side
rdt_send(): called from above, (e.g., by app.). Passed data to
deliver to receiver upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper
3.4 principles of reliable data transfer
implementation of rdt reliable data transfer protocol
implementation of rdt reliable data
transfer protocol
rdt_send ( )
deliver_data ( )
udt_send ( )
rdt_rcv ( )
unreliable channel
data
receiving
process
sending
process
data
Bi-directional communication over unreliable channel
data
packet
data
Header
data
Header

## Slide 28: Reliable data transfer: getting started
we'll:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow on both directions!
use finite state machines (FSM) to specify sender, receiver
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this "state" next state uniquely determined by next event
event
actions
3.4 principles of reliable data transfer

## Slide 29: rdt1.0: reliable transfer over a reliable channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver reads data from underlying channel
sender
receiver
3.4 principles of reliable data transfer
Wait for call from above
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
extract (packet,data)
deliver_data(data)
Wait for call from below
rdt_rcv(packet)

## Slide 30: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  feedback: control messages (ACK,NAK) from receiver → sender
3.4 principles of reliable data transfer
How do humans recover from "errors"
during conversation?
Repeat whenever there is a “pardon”
Notes: Acknowledge 确认

## Slide 31: rdt2.0: FSM specification
3.4 principles of reliable data transfer
Wait for call from above
udt_send(sndpkt)
rdt_rcv(rcvpkt) && isNAK(rcvpkt)
Wait for ACK or NAK
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
Wait for call from below
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
L
sender
receiver

## Slide 32: rdt2.0: FSM specification
3.4 principles of reliable data transfer
Wait for call from above
udt_send(sndpkt)
rdt_rcv(rcvpkt) && isNAK(rcvpkt)
Wait for ACK or NAK
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
Wait for call from below
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
L
sender
receiver
Note: "state" of receiver (did the receiver get my message correctly?) isn’t known to sender unless somehow communicated from receiver to sender
that’s why we need a protocol!

## Slide 33: rdt2.0: operation with no errors
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L
3.4 principles of reliable data transfer
sender
receiver

## Slide 34: rdt2.0: error scenario
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L
3.4 principles of reliable data transfer
receiver
sender

## Slide 35: rdt2.0 has a fatal flaw!
what happens if ACK/NAK corrupted?
sender doesn't know what happened at receiver!
can't just retransmit: possible duplicate
handling duplicates:
sender retransmits current pkt if ACK/NAK corrupted
sender adds sequence number to each pkt
receiver discards (doesn't deliver up) duplicate pkt
stop and wait
sender sends one packet,
then waits for receiver
response
3.4 principles of reliable data transfer

## Slide 36: rdt2.1: sender, handles garbled ACK/NAKs
3.4 principles of reliable data transfer
Wait for call 0 from above
Wait for ACK or NAK 0
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt) || isNAK(rcvpkt) )
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt) ||
isNAK(rcvpkt) )
Wait for
call 1 from above
Wait for ACK or NAK 1
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
L
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt) && isACK(rcvpkt)
L
Notes: garbley gook
gobbledygook

## Slide 37: rdt2.1: receiver, handles garbled ACK/NAKs
3.4 principles of reliable data transfer
Wait for
0 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)

## Slide 38: rdt2.1: discussion
sender:
seq # added to pkt
two seq. #s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must "remember" whether "expected" pkt should have seq # of 0 or 1
receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender
3.4 principles of reliable data transfer

## Slide 39: rdt2.2: a NAK-free protocol
same functionality as rdt2.1, using ACKs only
instead of NAK, receiver sends ACK for last pkt received OK
  receiver must explicitly include seq # of pkt being ACKed
duplicate ACK at sender results in same action as NAK: retransmit current pkt
3.4 principles of reliable data transfer
As we will see, TCP uses this approach to be NAK-free

## Slide 40: rdt2.2: sender, receiver fragments
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
Wait for ACK
0
sender FSM
fragment
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK1, chksum)
udt_send(sndpkt)
Wait for
0 from below
rdt_rcv(rcvpkt) &&
(corrupt(rcvpkt) ||
has_seq1(rcvpkt))
udt_send(sndpkt)
receiver FSM
fragment
L
3.4 principles of reliable data transfer

## Slide 41: rdt3.0: channels with errors and loss
new assumption: underlying channel can also lose packets (data, ACKs)
  checksum, seq. #, ACKs, retransmissions will be of help … but not enough
approach: sender waits "reasonable" amount of time for ACK
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
  retransmission will be duplicate, but seq. #'s already handles this
  receiver must specify seq # of pkt being ACKed
requires countdown timer
3.4 principles of reliable data transfer
How do humans handle lost sender-to-receiver words in conversation?

## Slide 42: rdt3.0 sender
3.4 principles of reliable data transfer
Wait for ACK0
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
stop_timer
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
udt_send(sndpkt)
start_timer
timeout
Wait for
call 0from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
L
rdt_rcv(rcvpkt)
L
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
udt_send(sndpkt)
start_timer
timeout
L

## Slide 43: rdt3.0 in action
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
pkt1
ack1
ack0
ack0
(a) no loss
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(b) packet loss
pkt1
X
loss
pkt1
timeout
resend pkt1
3.4 principles of reliable data transfer

## Slide 44: rdt3.0 in action
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(c) ACK loss
ack1
X
loss
pkt1
timeout
resend pkt1
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
send ack0
rcv ack0
send pkt1
send pkt0
rcv pkt0
pkt0
ack0
(d) premature timeout/ delayed ACK
pkt1
timeout
resend pkt1
ack1
send ack1
send pkt0
rcv ack1
pkt0
ack1
ack0
send pkt0
rcv ack1
pkt0
rcv pkt0
send ack0
ack0
rcv pkt0
send ack0
(detect duplicate)
3.4 principles of reliable data transfer

## Slide 45: Performance of rdt3.0
rdt3.0 is correct, but performance stinks
e.g.: 1 Gbps link, 15 ms prop. delay, 8000 bit packet:
  Usender: utilization – fraction of time sender busy sending
  if RTT=30 msec, 1KB pkt every 30 msec: 33kB/sec thruput over 1 Gbps link
network protocol limits use of physical resources!
Dtrans =
L
R
8000 bits
109 bits/sec
=
=
8 microsecs
3.4 principles of reliable data transfer
Notes: ms: millisecond 毫秒 = 0.001 second
microsecond微秒=0.000001 second

## Slide 46: rdt3.0: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
3.4 principles of reliable data transfer

## Slide 47: Pipelined protocols
pipelining: sender allows multiple, "in-flight", yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver
two generic forms of pipelined protocols: go-Back-N, selective repeat
3.4 principles of reliable data transfer

## Slide 48: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
3-packet pipelining increases
utilization by a factor of 3!
3.4 principles of reliable data transfer
81

## Slide 49: Pipelined protocols: overview
Go-back-N:
sender can have up to N unacked packets in pipeline
receiver only sends cumulative ack
  doesn't ack packet if there's a gap
sender has timer for oldest unacked packet
  when timer expires, retransmit all unacked packets
Selective Repeat:
sender can have up to N unack'ed packets in pipeline
rcvr sends individual ack for each packet
sender maintains timer for each unacked packet
  when timer expires, retransmit only that unacked packet
3.4 principles of reliable data transfer

## Slide 50: Go-Back-N: sender
k-bit seq # in pkt header
"window" of up to N, consecutive unack'ed pkts allowed
3.4 principles of reliable data transfer
already
ack’ed
sent, not yet ack’ed
usable, not yet sent
not usable
Window size
N
nextseqnum
ACK(n): ACKs all pkts up to, including seq # n - "cumulative ACK "
  may receive duplicate ACKs (see receiver)
timer for oldest in-flight pkt
timeout(n): retransmit packet n and all higher seq # pkts in window
send_base

## Slide 51: Go-Back-N: sender extended FSM
3.4 principles of reliable data transfer
Wait
start_timer
udt_send(sndpkt[base])
udt_send(sndpkt[base+1])
…
udt_send(sndpkt[nextseqnum-1])
timeout
rdt_send(data)
if (nextseqnum < base+N) {
sndpkt[nextseqnum] = make_pkt(nextseqnum,data,chksum)
udt_send(sndpkt[nextseqnum])
if (base == nextseqnum)
start_timer
nextseqnum++
}
else
refuse_data(data)
base = getacknum(rcvpkt)+1
If (base == nextseqnum)
stop_timer
else
start_timer
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
base=1
nextseqnum=1
rdt_rcv(rcvpkt)
&& corrupt(rcvpkt)
L

## Slide 52: Go-Back-N : receiver extended FSM
ACK-only: always send ACK for correctly-received pkt with highest in-order seq #
  may generate duplicate ACKs
  need only remember expectedseqnum
out-of-order pkt:
  discard (don't buffer): no receiver buffering!
  re-ACK pkt with highest in-order seq #
3.4 principles of reliable data transfer
Wait
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& hasseqnum(rcvpkt,expectedseqnum)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(expectedseqnum,ACK,chksum)
udt_send(sndpkt)
expectedseqnum++
udt_send(sndpkt)
any other event
expectedseqnum=1
sndpkt =
make_pkt(expectedseqnum,ACK,chksum)
L

## Slide 53: Go-Back-N in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, discard,
(re)send ack1
rcv ack0, send pkt4
rcv ack1, send pkt5
pkt 2 timeout
send pkt2
send pkt3
send pkt4
send pkt5
X
loss
receive pkt4, discard,
(re)send ack1
receive pkt5, discard,
(re)send ack1
rcv pkt2, deliver, send ack2
rcv pkt3, deliver, send ack3
rcv pkt4, deliver, send ack4
rcv pkt5, deliver, send ack5
ignore duplicate ACK
0 1 2 3 4 5 6 7 8
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
3.4 principles of reliable data transfer

## Slide 54: Selective repeat
receiver individually acknowledges all correctly received pkts
  buffers pkts, as needed, for eventual in-order delivery to upper layer
sender only resends pkts for which ACK not received
  sender timer for each unACKed pkt
sender window
  N consecutive seq #'s
  limits seq #s of sent, unACKed pkts
3.4 principles of reliable data transfer

## Slide 55: Selective repeat: sender, receiver windows
nextseqnum
3.4 principles of reliable data transfer
already
ack’ed
sent, not yet ack’ed
usable, not yet sent
not usable
Window size
N
send_base
Window size
N
not usable
expected, not yet received
out of order (buffered) but already ack’ed
acceptable
(within window)
(b) receiver view of sequence numbers
rcv_base
(a) sender view of sequence numbers

## Slide 56: Selective repeat
data from above:
if next available seq # in window, send pkt
timeout(n):
resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+N]:
mark pkt n as received
if n smallest unACKed pkt, advance window base to next unACKed seq #
sender
pkt n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer
in-order: deliver (also deliver buffered, in-order pkts), advance window to next not-yet-received pkt
pkt n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore
receiver
3.4 principles of reliable data transfer

## Slide 57: Selective repeat in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, buffer,
send ack3
rcv ack0, send pkt4
rcv ack1, send pkt5
pkt 2 timeout
send pkt2
X
loss
receive pkt4, buffer,
send ack4
receive pkt5, buffer,
send ack5
rcv pkt2; deliver pkt2,
pkt3, pkt4, pkt5; send ack2
record ack3 arrived
0 1 2 3 4 5 6 7 8
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
record ack4 arrived
record ack5 arrived
Q: what happens when ack2 arrives?
3.4 principles of reliable data transfer

## Slide 58: Selective repeat: dilemma
example:
seq #'s: 0, 1, 2, 3
window size=3
receiver window
(after receipt)
sender window
(after receipt)
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
timeout
retransmit pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
X
X
will accept packet
with seq number 0
(b) oops!
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
will accept packet
with seq number 0
0 1 2 3 0 1 2
pkt3
(a) no problem
receiver can't see sender side.
receiver behavior identical in both cases!
something's (very) wrong!
receiver sees no difference in two scenarios!
duplicate data accepted as new in (b)
Q: what relationship between seq # size and window size to avoid problem in (b)?
3.4 principles of reliable data transfer

## Slide 59: Homework
用 python 实现 UDP 的16位校验和，并用该程序验算课本3.3.2节的计算
第三章后作业选做2题
Transport Layer

## Slide 60
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
3.6 principles of congestion control
3.7 TCP congestion control
Transport Layer
Chapter 3 Transport Layer

## Slide 61
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
3.6 principles of congestion control
3.7 TCP congestion control
Transport Layer
Chapter 3 Transport Layer

## Slide 62: TCP: Overview RFCs: 793,1122,2018,5681,7323
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) initializes sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte steam:
  no "message boundaries"
pipelined:
  TCP congestion and flow control set window size
3.5 connection-oriented transport: TCP
Notes: 链路层 MTU : Maximum Transmission Unit

## Slide 63
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
3.6 principles of congestion control
3.7 TCP congestion control
Transport Layer
Chapter 3 Transport Layer

## Slide 64: TCP segment structure
IP header
IP data
TCP header
TCP data
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
receive window
Urg data pointer
checksum
F
S
R
P
A
U
head
len
not
used
options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept (rwnd)
counting by bytes of data
(not segments!)
Internet
checksum
(as in UDP)
3.5 connection-oriented transport: TCP
HLEN
4
RSVD
4
URG
ACK
PSH
RST
SYN
FIN
Flag field
ECE
CWR
CWR & ECE:
Explicit congestion
Notification (3.7.2)
CWR
ECE
data sent by application into TCP socket
urgent data (generally not used)
flow
control
Notes: not used (4)

## Slide 65: 3-Way Handshake
TCP requires connection establishment before data transfer begins.
For a connection to be established or initialized, the two hosts must synchronize their Initial Sequence Numbers (ISNs).
Connection Setup
3-way handshake
A
B
Syn
Syn + Ack
Ack
Connection Teardown
2 x 2-way handshake
A
B
Fin
Ack
Fin
Ack
Send SYN
(seq=x ctl=SYN)
SYN received
SYN received
Send SYN, ACK
(seq=y ack=x+1
ctl=SYN, ACK)
Established
(seq=x+1 ack=y+1
ctl=ACK)
3.5 connection-oriented transport: TCP
detailed description later in connection management …

## Slide 66: TCP seq. numbers, ACKs
sequence numbers:
  byte stream "number" of first byte in segment's data
acknowledgements:
  seq # of next byte expected from other side
  cumulative ACK
Q: how receiver handles out-of-order segments
  A: TCP spec doesn't say, - up to implementor
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
incoming segment to sender
A
sent
ACKed
sent, not-yet ACKed
("in-flight")
usable
but not
yet sent
not
usable
window size
N
  sender sequence number space
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from sender
3.5 connection-oriented transport: TCP

## Slide 67: TCP seq. numbers, ACKs
User
types
'C'
host ACKs
receipt
of echoed
'C'
host ACKs
receipt of
'C', echoes
back 'C'
simple telnet scenario
Host B
Host A
Seq=42, ACK=79, data = 'C'
Seq=79, ACK=43, data = 'C'
Seq=43, ACK=80
3.5 connection-oriented transport: TCP

## Slide 68: TCP round trip time, timeout
Q: how to set TCP timeout value?
longer than RTT
  but RTT varies
too short: premature timeout, unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT: measured time from segment transmission until ACK receipt
  ignore retransmissions
SampleRTT will vary, want estimated RTT "smoother"
  average several recent measurements, not just current SampleRTT
3.5 connection-oriented transport: TCP

## Slide 69: TCP round trip time, timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
exponential weighted moving average
influence of past sample decreases exponentially fast
typical value:  = 0.125
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)
3.5 connection-oriented transport: TCP

## Slide 70: TCP round trip time, timeout
timeout interval: EstimatedRTT plus "safety margin"
  large variation in EstimatedRTT： want a larger safety margin
estimate SampleRTT deviation from EstimatedRTT:
DevRTT = (1-)*DevRTT +
*|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
"safety margin"
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
3.5 connection-oriented transport: TCP

## Slide 71
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
3.6 principles of congestion control
3.7 TCP congestion control
Transport Layer
Chapter 3 Transport Layer

## Slide 72: TCP reliable data transfer
TCP creates process-to-process reliable transfer of segments on top of IP’s unreliable host-to-hos host delivery of IP datagram
  pipelining of segments
  cumulative acks
  single retransmission timer
retransmissions triggered by:
  timeout events
  duplicate acks
let's initially consider simplified TCP sender:
  ignore duplicate acks
  ignore flow control, congestion control
3.5 connection-oriented transport: TCP

## Slide 73: TCP sender events:
event: data rcvd from app
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running
  think of timer as for oldest unACKed segment
  expiration interval: TimeOutInterval
event: timeout
retransmit segment that caused timeout
restart timer
event: ACK rcvd
if ACK acknowledges previously unACKed segments
  update what is known to be ACKed
  start timer if there are still unACKed segments
3.5 connection-oriented transport: TCP

## Slide 74: TCP sender (simplified)
3.5 connection-oriented transport: TCP
wait
for
event
NextSeqNum = InitialSeqNum
SendBase = InitialSeqNum
L
retransmit not-yet-acked segment with smallest seq. #
start timer
timeout
if (y > SendBase) {
SendBase = y
/* SendBase–1: last cumulatively ACKed byte */
if (there are currently not-yet-acked segments)
start timer
else stop timer
}
ACK received, with ACK field value y
create segment, seq. #: NextSeqNum
pass segment to IP (i.e., "send")
NextSeqNum = NextSeqNum + length(data)
if (timer currently not running)
start timer
data received from application above

## Slide 75: TCP: retransmission scenarios
lost ACK scenario
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8 bytes of data
X
timeout
ACK=100
premature timeout
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8
bytes of data
timeout
ACK=120
Seq=100, 20 bytes of data
ACK=120
SendBase=100
SendBase=120
SendBase=120
SendBase=92
3.5 connection-oriented transport: TCP

## Slide 76: TCP: retransmission scenarios
X
cumulative ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=120, 15 bytes of data
timeout
Seq=100, 20 bytes of data
ACK=120
3.5 connection-oriented transport: TCP

## Slide 77: TCP ACK generation Recommendation [RFC 5681]
event at receiver
arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
arrival of in-order segment with
expected seq #. One other
segment has ACK pending
arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
arrival of segment that
partially or completely fills gap
TCP receiver action
delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
immediately send single cumulative
ACK, ACKing both in-order segments
immediately send duplicate ACK,
indicating seq. # of next expected byte
immediate send ACK, provided that
segment starts at lower end of gap
3.5 connection-oriented transport: TCP
Notes: duplicate ACK: 冗余ACK，ACK复本

## Slide 78: TCP fast retransmit
time-out period often relatively long:
  long delay before resending lost packet
detect lost segments via duplicate ACKs.
  sender often sends many segments back-to-back
  if segment is lost, there will likely be many duplicate ACKs. , so treat three duplicate ACKs in a row as a segment loss indicator
if sender receives 3 ACKs for same data
("triple duplicate resend unACKed segment with smallest seq #
  likely that unACKed segment lost, so don't wait for timeout
TCP fast retransmit
("triple duplicate ACKs"),
3.5 connection-oriented transport: TCP

## Slide 79: TCP fast retransmit
X
fast retransmit after sender
receipt of triple duplicate ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
timeout
ACK=100
ACK=100
ACK=100
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data
3.5 connection-oriented transport: TCP

## Slide 80
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
3.6 principles of congestion control
3.7 TCP congestion control
Transport Layer
Chapter 3 Transport Layer

## Slide 81: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
application
OS
receiver protocol stack
application copying/
removing data from
TCP socket buffers ….
… slower than TCP
receiver is delivering
(sender is sending)
from sender
receiver controls sender, so sender won't overflow receiver's buffer by transmitting too much, too fast
flow control
3.5 connection-oriented transport: TCP
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
Network layer delivering IP datagram payload into TCP socket buffers
zero-copy
Notes: 在次介绍一下 zero-copy

## Slide 82: TCP flow control
buffered data
free buffer space
rwnd
RcvBuffer
TCP segment payloads
to application process
TCP receiver "advertises" free buffer space by including rwnd value in TCP header of receiver-to-sender segments
  RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems autoadjust RcvBuffer
sender limits amount of unACKed ("in-flight") data to receiver's rwnd value
guarantees receive buffer will not overflow
TCP
receiver-side buffering
3.5 connection-oriented transport: TCP
source port #
dest port #
application
data
(variable length)
sequence number
acknowledgement number
receive window
Urg data pointer
checksum
F
S
R
P
A
U
head
len
not
used
options (variable length)
ECE
CWR

## Slide 83
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
3.6 principles of congestion control
3.7 TCP congestion control
Transport Layer
Chapter 3 Transport Layer

## Slide 84: Connection Management
before exchanging data, sender/receiver "handshake":
agree to establish connection (each knowing the other willing to establish connection)
agree on connection parameters
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
Socket clientSocket =
newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();
3.5 connection-oriented transport: TCP

## Slide 85: Agreeing to establish a connection
Q: will 2-way handshake always work in network?
variable delays
retransmitted messages (e.g. req_conn(x)) due to message loss
message reordering
can't "see" other side
2-way handshake:
Let's talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
3.5 connection-oriented transport: TCP

## Slide 86: Agreeing to establish a connection
2-way handshake failure scenarios:
retransmit
req_conn(x)
ESTAB
req_conn(x)
half open connection!
(no client!)
client terminates
server
forgets x
connection
x completes
retransmit
req_conn(x)
ESTAB
req_conn(x)
data(x+1)
retransmit
data(x+1)
accept
data(x+1)
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
client terminates
ESTAB
choose x
req_conn(x)
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
connection
x completes
server
forgets x
3.5 connection-oriented transport: TCP

## Slide 87: TCP 3-way handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYNSENT
ESTAB
SYN RCVD
client state
LISTEN
server state
LISTEN
3.5 connection-oriented transport: TCP

## Slide 88: TCP 3-way handshake: FSM
closed
L
listen
SYN
rcvd
SYN
sent
ESTAB
Socket clientSocket =
newSocket("hostname","port number");
SYN(seq=x)
Socket connectionSocket = welcomeSocket.accept();
SYN(x)
SYNACK(seq=y,ACKnum=x+1)
create new socket for
communication back to client
SYNACK(seq=y,ACKnum=x+1)
ACK(ACKnum=y+1)
ACK(ACKnum=y+1)
L
3.5 connection-oriented transport: TCP

## Slide 89: TCP: closing a connection
client, server each close their side of connection
  send TCP segment with FIN bit = 1
respond to received FIN with ACK
  on receiving FIN, ACK can be combined with own FIN
simultaneous FIN exchanges can be handled
3.5 connection-oriented transport: TCP

## Slide 90: TCP: closing a connection
FIN_WAIT_2
CLOSE_WAIT
FINbit=1, seq=y
ACKbit=1; ACKnum=y+1
ACKbit=1; ACKnum=x+1
wait for server
close
can still
send data
can no longer
send data
LAST_ACK
CLOSED
TIMED_WAIT
timed wait
for 2*max
segment lifetime
CLOSED
FIN_WAIT_1
FINbit=1, seq=x
can no longer
send but can
receive data
clientSocket.close()
client state
server state
ESTAB
ESTAB
3.5 connection-oriented transport: TCP

## Slide 91
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
3.6 principles of congestion control
3.7 TCP congestion control
Chapter 3 Transport Layer
Transport Layer

## Slide 92: Principles of congestion control
congestion:
informally: "too many sources sending too much data too fast for network to handle"
different from flow control!
manifestations:
  lost packets (buffer overflow at routers)
  long delays (queueing in router buffers)
a top-10 problem!
3.6 principles of congestion control
Notes: manifestation – 表现形式

## Slide 93: Causes/costs of congestion: scenario 1
3.6 principles of congestion control
Scenario:
two senders, two receivers
one router, infinite buffers
output link capacity: R
no retransmission
maximum per-connection throughput: R/2
unlimited shared output link buffers
Host A
Host B
throughput: lout
R/2
R/2
lout
lin
R/2
delay
lin
large delays as arrival rate lin approaches capacity
Q: What happens as arrival rate lin approaches R/2?
original data: lin

## Slide 94: Causes/costs of congestion: scenario 2
one router, finite buffers
sender retransmission of timed-out packet
  application-layer input = application-layer output: lin = lout
  transport-layer input includes retransmissions : lin lin
finite shared output link buffers
Host A
lin : original data
Host B
lout
l'in: original data, plus retransmitted data
'
3.6 principles of congestion control

## Slide 95: Causes/costs of congestion: scenario 2
idealization: perfect knowledge
sender sends only when router buffers available
R/2
R/2
lout
lin
3.6 principles of congestion control
finite shared output link buffers
lin : original data
lout
l'in: original data, plus retransmitted data
copy
free buffer space!
Host B
Host A

## Slide 96: Causes/costs of congestion: scenario 2
Idealization: some perfect knowledge
packets can be lost (dropped at router) due to full buffers
sender knows when packet has been dropped: only resends if packet known to be lost
3.6 principles of congestion control
lin : original data
lout
l'in: original data, plus retransmitted data
copy
no buffer space!
Host B
Host A

## Slide 97: Causes/costs of congestion: scenario 2
Idealization: some perfect knowledge
packets can be lost (dropped at router) due to full buffers
sender knows when packet has been dropped: only resends if packet known to be lost
3.6 principles of congestion control
lin : original data
lout
l'in: original data, plus retransmitted data
free buffer space!
Host B
Host A
R/2
R/2
lin
lout
when sending at R/2, some packets are retransmissions but asymptotic goodput is still R/2 (why?)

## Slide 98: Causes/costs of congestion: scenario 2
3.6 principles of congestion control
lin
lout
l'in
copy
free buffer space!
timeout
Host B
R/2
R/2
lin
lout
when sending at R/2, some packets are retransmissions including duplicated that are delivered!
Realistic scenario: duplicates are sent
packets can be lost, dropped at router due to full buffers – requiring retransmissions
but sender times can time out prematurely, sending two copies, both of which are delivered
Host A

## Slide 99: Causes/costs of congestion: scenario 2
R/2
lout
when sending at R/2, some packets are retransmissions including duplicated that are delivered!
"costs" of congestion:
more work (retrans) for given "goodput"
unneeded retransmissions: link carries multiple copies of pkt
  decreasing goodput
R/2
lin
Realistic: duplicates
packets can be lost, dropped at router due to full buffers
sender times out prematurely, sending two copies, both of which are delivered
3.6 principles of congestion control

## Slide 100: Causes/costs of congestion: scenario 3
four senders
multi-hop paths
timeout/retransmit
Q: what happens as and increase ?
finite shared output link buffers
Host A
lout
Host B
Host C
Host D
lin : original data
l'in: original data, plus retransmitted data
A: as red increases, all arriving blue pkts at upper queue are dropped, blue throughput g 0
3.6 principles of congestion control
R3
R1
R2
R4

## Slide 101: Causes/costs of congestion: scenario 3
another "cost" of congestion:
when packet dropped, any "upstream" transmission capacity used for that packet was wasted!
C/2
C/2
lout
lin'
3.6 principles of congestion control
Notes: upstream: 上游

## Slide 102
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
3.6 principles of congestion control
3.7 TCP congestion control
Chapter 3 Transport Layer
Transport Layer

## Slide 103: TCP congestion control: additive increase multiplicative decrease
approach: sender increases transmission rate (window size, cwnd), probing for usable bandwidth, until loss occurs
  Additive Increase: increase cwnd by 1 MSS every RTT until loss detected
  Multiplicative Decrease: cut cwnd in half after loss
cwnd: TCP sender
congestion window size
AIMD saw tooth
behavior: probing
for bandwidth
additively increase window size …
…. until loss occurs (then cut window in half)
time
3.7 TCP congestion control
AIMD
Maximum Segment Size
"AIMD"
also known as "congestion avoidance"

## Slide 104: TCP Congestion Control: details
sender limits transmission:
cwnd is dynamic, function of perceived network congestion
TCP sending rate:
roughly: send cwnd bytes, wait RTT for ACKS, then send more bytes
last byte
ACKed
sent, not-yet ACKed
("in-flight")
cwnd
last byte sent
sender sequence number space
bytes/sec
3.7 TCP congestion control
available but not used

## Slide 105: TCP Slow Start
when connection begins, increase rate exponentially until first loss event:
  initially cwnd = 1 MSS
  double cwnd every RTT
  done by incrementing cwnd for every ACK received
summary: initial rate is slow but ramps up exponentially fast
Host A
one segment
Host B
RTT
time
two segments
four segments
3.7 TCP congestion control

## Slide 106: TCP: detecting, reacting to loss
loss indicated by timeout:
  cwnd set to 1 MSS;
  window then grows exponentially (as in slow start) to threshold, then grows linearly
loss indicated by 3 duplicate ACKs: TCP RENO
  dup ACKs indicate network capable of delivering some segments
  cwnd is cut in half window then grows linearly
TCP Tahoe always sets cwnd to 1 (timeout or 3 duplicate acks)
3.7 TCP congestion control
Notes: 慢启动
拥塞避免模式
快恢复

## Slide 107: TCP: switching from slow start to CA
Q: when should the exponential increase switch to linear?
A: when cwnd gets to 1/2 of its value before timeout.
Implementation:
variable ssthresh
on loss event, ssthresh is set to 1/2 of cwnd just before loss event
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
3.7 TCP congestion control

## Slide 108: Summary: TCP Congestion Control
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
L
cwnd > ssthresh
congestion
avoidance
cwnd = cwnd + MSS (MSS/cwnd)
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
.
dupACKcount++
duplicate ACK
fast
recovery
cwnd = cwnd + MSS
transmit new segment(s), as allowed
duplicate ACK
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
timeout
ssthresh = cwnd/2
cwnd = 1
dupACKcount = 0
retransmit missing segment
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
cwnd = ssthresh
dupACKcount = 0
New ACK
slow
start
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
cwnd = cwnd+MSS
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
dupACKcount++
duplicate ACK
L
cwnd = 1 MSS
ssthresh = 64 KB
dupACKcount = 0
New
ACK!
New
ACK!
New
ACK!
3.7 TCP congestion control

## Slide 109: TCP throughput
avg. TCP thruput as function of window size, RTT?
  ignore slow start, assume always data to send
W: window size (measured in bytes) where loss occurs
  avg. window size (# in-flight bytes) is ¾ W
  avg. thruput is 3/4W per RTT
W
W/2
avg TCP thruput =
3
4
W
RTT
bytes/sec
3.7 TCP congestion control

## Slide 110: TCP Futures: TCP over "long, fat pipes"
example: 1500 byte segments, 100ms RTT, want 10 Gbps throughput
requires W = 83,333 in-flight segments
throughput in terms of segment loss probability, L [Mathis 1997]:
  ➜ to achieve 10 Gbps throughput, need a loss rate of L = 2·10-10 – a very small loss rate!
new versions of TCP for high-speed
TCP throughput =
1.22
.
MSS
RTT
L
3.7 TCP congestion control

## Slide 111: TCP and the congested “bottleneck link”
TCP (classic, CUBIC) increase TCP’s sending rate until packet loss occurs at some router’s output: the bottleneck link
source
application
TCP
network
link
physical
destination
application
TCP
network
link
physical
bottleneck
link is always busy
packet queue almost never empty, sometimes overflows packet (loss)
3.7 TCP congestion control

## Slide 112: TCP and the congested “bottleneck link”
TCP (classic, CUBIC) increase TCP’s sending rate until packet loss occurs at some router’s output: the TCP bottleneck link
source
application
TCP
network
link
physical
destination
application
TCP
network
link
physical
understanding congestion: useful to focus on congested bottleneck link
insight: increasing TCP sending rate will not increase end-end throughout with congested bottleneck
insight: increasing TCP sending rate will increase measured RTT
RTT
Goal: “keep the end-end pipe just full, but not fuller”
3.7 TCP congestion control

## Slide 113: Delay-based TCP Congestion Control
Keeping sender-to-receiver pipe “just full enough, but no fuller”: keep bottleneck link busy transmitting, but avoid high delays/buffering
RTTmeasured
Delay-based approach:
RTTmin - minimum observed RTT (uncongested path)
ideal throughput with congestion window cwnd is cwnd/RTTmin
if measured throughput “very close” to ideal throughput
increase cwnd /* since path not congested */
else if measured throughput “far below” ideal throughout
increase cwnd /* since path is congested */
RTTmeasured
measured
throughput
=
# bytes sent in last RTT interval
3.7 TCP congestion control

## Slide 114: Delay-based TCP Congestion Control
congestion control without inducing/forcing loss
maximizing throughout (“keeping the just pipe full… ”) while keeping delay low (“…but not fuller”)
a number of deployed TCPs take a delay-based approach
  BBR deployed on Google’s (internal) backbone network
3.7 TCP congestion control

## Slide 115: Explicit Congestion Notification (ECN)
source
application
TCP
network
link
physical
destination
application
TCP
network
link
physical
network-assisted congestion control:
two bits in IP header (ToS field) marked by network router to indicate congestion
policy to determine marking chosen by network operator
congestion indication carried to receiving host
receiver (seeing congestion indication in IP datagram) ) sets ECE bit on receiver-to-sender ACK segment to notify sender of congestion
ECN=00
ECN=11
ECE=1
IP datagram
TCP ACK segment
3.7 TCP congestion control

## Slide 116: TCP Fairness
fairness goal: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck
router
capacity R
TCP connection 2
3.7 TCP congestion control

## Slide 117: Q: Is TCP fair?
Example: two competing sessions:
additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2
3.7 TCP congestion control
A: Yes, under idealized assumptions:
same RTT
fixed number of sessions only in congestion avoidance
Is TCP fair?

## Slide 118: Fairness: must all network apps be “fair”?
Fairness and UDP
multimedia apps often do not use TCP
  do not want rate throttled by congestion control
instead use UDP:
  send audio/video at constant rate, tolerate packet loss
there is no “Internet police” policing use of congestion control
Fairness, parallel TCP connections
application can open multiple parallel connections between two hosts
web browsers do this
e.g., link of rate R with 9 existing connections:
  new app asks for 1 TCP, gets rate R/10
  new app asks for 11 TCPs, gets R/2
3.7 TCP congestion control

## Slide 119: Explicit Congestion Notification (ECN)
network-assisted congestion control:
two bits in IP header (ToS field) marked by network router to indicate congestion
congestion indication carried to receiving host
receiver (seeing congestion indication in IP datagram) ) sets ECE bit on receiver-to-sender ACK segment to notify sender of congestion
source
application
transport
network
link
physical
destination
application
transport
network
link
physical
ECN=11
ECN=00
ECN=11
ECE=1
IP datagram
TCP ACK segment
3.7 TCP congestion control

## Slide 120: QUIC: Quick UDP Internet Connections
application-layer protocol, on top of UDP
  to increase performance of HTTP
  deployed on many Google servers, apps (Chrome, mobile YouTube app)
adopts approaches we’ve studied in this chapter for connection establishment, error control, congestion control
  connection establishment handshake: performs authentication, encryption key management while establishing error/congestion control state, avoiding RTT delays
  error and congestion control: ““Readers familiar with TCP’s loss detection and congestion control will find algorithms here that parallel well-known TCP ones.” [from QUIC specification]
3.7 TCP congestion control

## Slide 121: QUIC: Quick UDP Internet Connections
multiple application-level “streams” multiplexed in parallel over single QUIC connection
  e.g. each stream could be an HTTP object from Web server to client (recall HTTP and TCP/HOL blocking)
IP
TCP
TLS
HTTP/2
IP
UDP
QUIC
HTTP/2 (slimmed)
Network
Transport
Application
HTTP/2 over TCP
HTTP/3
HTTP/3 over QUIC over UDP
3.7 TCP congestion control

## Slide 122: QUIC: Streams: parallelism, no HOL blocking
(a) HTTP 1.1
TLS encryption
TCP RDT
TCP Cong. Contr.
transport
application
(b) HTTP/2 with QUIC: no HOL blocking
TCP RDT
TCP Cong. Contr.
TLS encryption
error!
HTTP
GET
HTTP
GET
HTTP
GET
QUIC Cong. Cont.
QUIC
encrypt
QUIC
RDT
QUIC
RDT
QUIC
RDT
QUIC
encrypt
QUIC
encrypt
UDP
UDP
QUIC Cong. Cont.
QUIC
encrypt
QUIC
RDT
QUIC
RDT
QUIC
RDT
QUIC
encrypt
QUIC
encrypt
error!
HTTP
GET
HTTP
GET
HTTP
GET
3.7 TCP congestion control

## Slide 123: Chapter 3: summary
principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
instantiation, implementation in the Internet
  UDP
  TCP
next:
leaving the network "edge" (application, transport layers)
into the network "core"
two network layer chapters:
  data plane
  control plane
Transport Layer

## Slide 124: Homework
用 python 完成一个演示TCP拥塞控制的小程序
或
第三章后作业选做3题（含一道拥塞控制的问题）
Transport Layer